## Slide 1: PRODUCTION TECHNOLOGY (MEC-303A)
Dr. Mukesh Kumar
Assistant Professor (Guest Faculty)
Mechanical Engineering Department
B.Tech. 5th Semester
Unit-1 (b)

## Slide 2: Machining Processes and Machine Tools
Machining is the removal of material and modification of the surfaces of a workpiece
Machining involves secondary and finishing operations

## Slide 3: Machining Processes and Machine Tools
Major types of material removal processes:
Cutting
Abrasive processes
Advanced machining processes
Machining operations is a system consisting of the
Workpiece
Cutting tool
Machine tool
Production personnel
Copyright © 2010 Pearson Education South Asia Pte Ltd

## Slide 4: Classification of material removal process

## Slide 5: Types of Machining Operation
Cutting processes remove material from the surface of a workpiece by producing chips
Common cutting processes:
Turning (workpiece rotates; tool moves left, removes layer of material)
Cutting off (cutting tool moves radially inward)
Slab milling (rotating cutting tool removes material from workpiece)
End milling (rotating cutter; produces cavity)
Copyright © 2010 Pearson Education South Asia Pte Ltd

## Slide 6: Types of Machining Operation
In the turning process, the cutting tool is set at a certain depth of cut [mm] and travels to the left (with a certain velocity) as the workpiece rotates
Feed, or feed rate, is the distance the tool travels horizontally per unit revolution of the workpiece [mm/rev]
  This tool movement produces chips, which move up the face of the tool
Copyright © 2010 Pearson Education South Asia Pte Ltd

## Slide 7: Theory of Chip Formation in Metal Cutting
In idealized model, a cutting tool moves to the left along the workpiece at a constant velocity, V, and a depth of cut, to
Chip thickness, tc
Copyright © 2010 Pearson Education South Asia Pte Ltd
Idealized model; Orthogonal; 2-D cutting with a well-defined shear plane; also called M.E. Merchant model
Orthogonal (2-D) cutting without a well-defined shear plane: “shear zone”; why rough surface?